## Slide 1: 17. Inter-Domain Routing
General Concepts
BGP
Roch Guerin
(with adaptations from Jon Turner and John DeHart, and material from Kurose and Ross)

## Slide 2: Hierarchical Routing
The Internet is divided among many distinct networks
  owned and operated by different organizations
  networks called Autonomous Systems (aka routing domains)
Leads to a two level routing structure
  intra-domain routing: finding most efficient paths within an AS
  inter-domain routing: finding paths among ASes
  makes Internet routing more scalable
  allows ASes to operate independently and to keep their internal network structure private
Drawbacks of hierarchical routing
  lack of global knowledge of network topology prevents selection of best routes
  motivates AS-owners to focus on reducing their own costs, not providing best service to users

## Slide 3: Routing Protocols
AS 524
A two-level hierarchy for routing protocols
  Interior Gateway Protocols (IGP) control routing within an AS/domain
  Exterior Gateway Protocols (EGP) control routing between AS’s
Different goals and constraints for each family of protocols
  IGP: Ability to fine tune internal operation and shielding from outside “noise”
  EGP: Scalability and ability to accommodate a broad range of administrative policies
AS 121
AS 1
AS 2
AS 3
AS 123
AS 3411
AS 321
AS 168
AS 376
AS 441

## Slide 4: Inter-AS Tasks
Suppose router in AS1 receives datagram destined outside of AS1
  router should forward packet to gateway router, but which one?
AS1 must:
learn which destinations are reachable through AS2, which through AS3
propagate this reachability info to all routers in AS1
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks

## Slide 5: Internet Inter-Domain Routing: BGP
BGP (Border Gateway Protocol): the de facto inter-domain routing protocol
  “glue that holds the Internet together”
BGP provides each AS a means to:
  advertise internal subnets to the rest of Internet
  obtain subnet reachability information from neighboring ASes – eBGP
  propagate reachability information to all AS-internal routers
    iBGP
    ? iBGP vs. IGP ?
      iBGP is between routers within an AS
      IGP is between routers within an AS
      Why both?
  determine “good” routes to other networks based on reachability information and policy.

## Slide 6: BGP Overview
BGP operation and terminology
  Identifies domains by unique Autonomous System (AS) numbers
  Allows AS connectivity of arbitrary topology
  BGP speakers exchange routes and their attributes
BGP as a protocol is relatively simple (104 pages for the latest draft vs 244 for OSPF), but its configuration can be complex and errors can have far-reaching implications
  Freedom to customize your decisions means more opportunities to make bad decisions…

## Slide 7: BGP Overview (continued)
Major BGP features
  Selection of “best” path based on routes attributes and driven primarily by local criteria (I set my own preferences)
    Each AS is free to use different selection criteria with a few exceptions for “global” precedence rules
  Distinguishes exchange of information between internal and external border routers (BGP peers)
    Internal peers: within the same domain
    External peers: in adjacent domains
  Loop avoidance (path vectors)
  Scalability through route aggregation

## Slide 8: BGP Operation Summary
Three major phases
Neighbor acquisition and liveness monitoring
  List of BGP neighbors must be configured in each router
  BGP connection initiated with OPEN message and maintained by KEEPALIVE messages (sent over TCP – port 179)
    Each side must send an OPEN message
    Neighbor declared unreachable if no KEEPALIVE received within Holding Time
Routing information exchanged through UPDATE messages
  Initial exchange followed by incremental updates for changes & withdrawals of routes
    Reliability through TCP
  Not all neighbors receive the same information (export policies)
    Policies need to be configured for each neighbor
Path selection uses policies (local rules) and route information received in UPDATE messages from all peers to select the “best” path for a route and construct the BGP routing table

## Slide 9: A Typical BGP Configuration
Two types of connections between BGP routers (peers) based on whether they are in the same or different ASes
  Routers in different ASes establish an external BGP (eBGP) connection
    Send subset (based on policies) of own routing table to eBGP peers
  Routers in the same AS establish an internal BGP (iBGP) connection
    iBGP peers typically connected by full mesh (more on this later)
    Send only own (local or from eBGP) information, not that of iBGP peers
iBGP
iBGP
iBGP
iBGP
iBGP
iBGP
eBGP
eBGP
eBGP
eBGP
eBGP
AS 1
AS 2
AS 3
Rtr A1
Rtr B1
Rtr A2
Rtr B2
Rtr A3
Rtr B3
Rtr D2
Rtr C2

## Slide 10: BGP UPDATE Message
UPDATE message is the basic unit of route advertisement
  Can contain multiple routes being withdrawn
    As specified in Unfeasible Route Length
  Path Attributes describe a number of key properties of the advertised route that are used to select the best path
  NLRI lists IP prefixes that share the Path Attributes
Unfeasible Route Length (2 bytes)
Withdrawn Routes (variable)
Total Path Attribute Length (2 bytes)
Path Attributes (variable)
Network Layer Reachability Information (NLRI) (variable)

## Slide 11: Path Attributes
Terminology examples:
  Well-known Mandatory: Must be recognized by all BGP speakers and must be carried in all updates
  Well-known Discretionary: Must be recognized by all BGP speakers and may be carried in updates but not required
  Optional Transitive: May be recognized by some BGP speakers but not all and should be preserved and transmitted to all peers.
  Optional Non-Transitive: May be recognized by some BGP speakers but not all, unrecognized attributes should not be passed along to peers.
  Other combinations possible …

## Slide 12: Key Path Attributes
LOCAL_PREF
  Well-known, discretionary, non-transitive
  Advertised only to iBGP peers to indicate degree of preference of a route by the advertising router (higher value is preferred)
MULTI_EXIT_DISC (MED)
  Optional, non-transitive (not propagated to other ASes)
  Advertised to eBGP peers to indicate preference for entry points into the AS (lower value is preferred)

## Slide 13: Key Path Attributes (continued)
AS_PATH
  Well-known, mandatory
  Sequence of path segments of type AS_SET (1) or AS_SEQUENCE (2)
    AS_SEQUENCE: Ordered list of ASes traversed by the route
    AS_SET: Unordered list of ASes traversed by the route
      (used when aggregating several routes)
  Updated by “pre-pending” own AS number when advertising to a BGP speaker in another AS  Loop prevention
NEXT_HOP
  Well-known, mandatory
  IP address of border router to be used as next hop towards destinations identified in the NLRI field
  Typically chosen to ensure that the “shortest” path is taken

## Slide 14: BGP Processing Steps
Phase 1
Reject unacceptable paths and determine degree of preference
Phase 3
Determine which routes to advertise based on policies
RIB_In
Rtr A2
RIB_In
Rtr B2
RIB_In
Rtr C2
RIB_In
Rtr A3
RIB_In
Rtr B3
Local RIB
RIB_Out
Rtr A2
RIB_Out
Rtr B2
RIB_ Out
Rtr C2
RIB_ Out
Rtr A3
RIB_ Out
Rtr B3
eBGPIN
eBGPOUT
iBGPOUT
iBGPIN
Router D2
Notes on phases on next slide
Export
Filters
Local RIB
–
RIB_In’s
Phase 2
Select best routes to install in LocRIB

## Slide 15: BGP Decision Process
Three phase process
  Phase 1: Calculates a “degree of preference” for each route in a given RIB_In (locks the associated RIB_In)
    If route is learned from a local peer (iBGP), the LOCAL_PREF attribute is usually taken as the degree of preference
    If route is learned from an external peer (eBGP), the degree of preference is computed based on local policy
      The resulting value is used as LOCAL_PREF in any subsequent iBGP advertisement
  Phase 2: Selects the “best” route out of all those available for a given destination (locks all RIB_In)
    Excludes routes with unresolvable NEXT_HOP (IGP does not know how to get there) or a loop in the AS_PATH attribute
    Best routes are installed in the Local RIB (one per destination)
  Phase 3: Decides, based on policies, which routes in Local RIB to advertise to which peer (blocks execution of Phase 2)
    Route aggregation can be performed at this stage

## Slide 16: BGP Selection Tie Breaking Rules
BGP selects a SINGLE route
  Prefer routes with the highest weight (local configuration)
  Prefer routes with the highest LOCAL_PREF value
  Prefer locally originated routes (by the router itself)
    Locally also implies local to the AS itself.
  Prefer routes with the smallest number of AS numbers in AS_PATH (each AS_SET counts only as one!)
  Prefer routes with the lowest ORIGIN value
  Among routes learned from the same neighboring AS, remove routes with less desirable (higher) MED values
  If at least one route was learned through eBGP, remove all routes learned through iBGP
  Prefer routes with minimum IGP cost to NEXT_HOP
  Prefer routes advertised by the BGP speaker with the lowest BGP identifier (ROUTER_ID)
    Prefer the route received from the lowest peer address

## Slide 17: Using LOCAL_PREF to Pick an Exit Point
Choosing between a primary and a backup provider
  Used to influence internal decisions
AS 2
AS 3
AS 1
AS 10
AS 11
Primary
Backup
LOCAL_PREF=20
LOCAL_PREF=100

## Slide 18: Influencing Entry Points
MED allows crude selection ability
  Avoid low speed internal links
But not always taken into account
AS 1
AS 111
19.2.1.0/24
19.2.0.0/24
AS 55
Low speed RF link
19.2.1.0/24; MED 5
19.2.0.0/24, MED 100
19.2.1.0/24; MED 100
19.2.0.0/24, MED 5

## Slide 19: Ignoring MED Values
Hot potato routing
  Basic rule: pick closest exit
  “I wont carry your bits for you…”
Level 3
AT&T
AT&T Customer
Level 3 Customer

## Slide 20: Policy-Based Control of Route Advertisements
AS 1
AS 2
AS 3
AS 6
AS 7
AS 5
AS 4
0.0.0.0/0
0.0.0.0/0
0.0.0.0/0
0.0.0.0/0
AS 1, AS 6
AS 1, AS 6
The safest way to ensure you don’t use me to reach a certain destination is by not telling you that I can reach it…
Outbound policies determine what reachability information I send to whom

## Slide 21: Common BGP Policies
Route preferences:
  customer routes
  peer routes
  provider routes
No valley paths
  Do not advertise routes learned from peers or providers to other peers or providers
An important concern in BGP is routing safety and robustness
  Do distributed BGP decisions always converge and does this remain true in the presence of changes/failures?
The answer is complex, but adherence to the above policies has been shown to ensure both safety and robustness (in the absence of relationship cycles)

## Slide 22: Intra-Domain & Inter-Domain Collaboration for End-to-End Forwarding
Forwarding table configured by both intra-domain and inter-domain routing
  intra-domain sets entries for internal destinations
  both collaborate to set entries for external destinations
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
intra-domain
routing
inter-domain
routing
Forwarding
table
3c
gateway router

## Slide 23: From BGP+IGP to Packet Forwarding Decisions
Recursive lookup for route r at router 1.1.1.1
  BGP routing table points to router 1.1.5.1 as NEXT_HOP for r
  IGP routing table identifies interface 10.2.1.1 on Router 1.1.2.1 as (local) next hop towards Router 1.1.5.1
  Forwarding table entry for route r directly points to 10.2.1.1
What happens when packet reaches router 1.1.2.1?
  Next slides…
AS 1
AS 2
AS 3
Router 1.1.1.1
r
Router 1.1.5.1
10.2.1.1
Router 1.1.2.1
Router 1.1.3.1
Router 1.1.4.1
iBGP
IGP

## Slide 24: BGP and IGP Collaboration
Two scenarios
  A translation step: From BGP to IGP (some internal routers do not speak BGP)
  A common language: All routers speak BGP (common in ISPs)
Scenario 1: BGP gateways and IGP-only internal routers
  BGP speakers participate in IGP and “export” into IGP routes they learn from BGP (or some suitable aggregates)
    Example of OSPF ASBRs (BGP routes → T5 external LSAs)
Scenario 2: all routers speak BGP+IGP
  Forwarding table can be constructed simply based on recursive lookup (only one lookup needed in final forwarding table, i.e., it contains the result of the recursive lookup)
    BGP associates routes to NEXT_HOP (exit point)
    IGP identifies local path to exit point

## Slide 25: Scenario 1 – Translation
BGP routes imported into IGP, e.g., OSPF
  Routers 1.1.1.1 and 1.1.5.1 are both BGP speakers and also participate in OSPF as ASBRs
  Router 1.1.5.1. learns of r through eBGP and advertises it in OSPF through a T5 LSA (external route r)
  Routers 1.1.2.1, 1.1.3.1 and 1.1.4.1 learn about r through the T5 LSA advertised by 1.1.5.1
  Router 1.1.1.1 learns about r through both BGP and OSPF (consistency, precedence?)
AS 1
AS 2
AS 3
Router 1.1.1.1
r
Router 1.1.5.1
10.2.1.1
Router 1.1.2.1
Router 1.1.3.1
Router 1.1.4.1
T5: < r >

## Slide 26: Scenario 2 – Common Language
All routers participate in BGP
  Routers 1.1.1.1 to 1.1.8.1 all know that 1.1.8.1 is the desired exit point and forward packets accordingly
AS 1
AS 2
AS 3
Router 1.1.1.1
r
Router 1.1.8.1
10.2.1.1
Router 1.1.3.1
Router 1.1.4.1
Router 1.1.6.1
Router 1.1.2.1
Router 1.1.5.1
Router 1.1.7.1

## Slide 27: BGP Example
AS1 1.1.*
AS6 6.6.*
AS7 7.7.*
AS5 5.5.*
AS4 4.4.*
AS3 3.3.*
AS2 2.2.*
A
E
C
B
D
AS8 8.8.*
AS9 9.9.*
6
11
8
7
9
10
5
3.3.1.1
7.7.2.1
2.2.1.1
7.7.1.1
5.5.1.1
.1.*
.2.*
.3.*
.4.*
.5.*

## Slide 28: Exercises
Use the diagram on the previous slide for the next questions.
List five distinct inter-AS paths leading to AS4 that router C might learn of using BGP. For each path, give the path and the “next-hop-address” for that path. For each of these inter-AS paths, what is the intra-AS path that would be used with it? Which path would you expect it to actually select? How would the selected path change if the costs of the AC and BC links both increased by 20? What if they increased by 1000?

## Slide 29: Exercises
Use the diagram on the previous slide for the next questions.
List five distinct inter-AS paths leading to AS4 that router C might learn of using BGP. For each path, give the path and the “next-hop-address” for that path. For each of these inter-AS paths, what is the intra-AS path that would be used with it? Which path would you expect it to actually select? How would the selected path change if the costs of the AC and BC links both increased by 20? What if they increased by 1000?
AS1 1.1.*
AS6 6.6.*
AS7 7.7.*
AS5 5.5.*
AS4 4.4.*
AS3 3.3.*
AS2 2.2.*
A
E
C
B
D
AS8 8.8.*
AS9 9.9.*
6
11
8
7
9
10
5
3.3.1.1
7.7.2.1
2.2.1.1
7.7.1.1
5.5.1.1
.1.*
.2.*
.3.*
.4.*
.5.*
  Possible paths in the format: AS_PATH; NEXT_HOP; AS1 intra-AS path (cost), are:
  AS4-AS2; router A; C-A (cost of 6)
  AS4-AS3; router B; C-B (cost of 9)
  AS4-AS2-AS8-AS9-AS7; router D, C-A-D or C-E-D (cost of 13)
  AS4-AS2-AS8-AS9-AS7; router E, C-E (cost of 5)
  AS4-AS2-AS8-AS9-AS7-AS6-AS5; router E, C-E (cost of 5)
  Note that the path AS4-AS2-AS8-AS9-AS7-AS6-AS5 through router E is not a path that router C learns about since router E will typically (barring any policy over-ride) prefer the shorter AS_PATH length of the path that goes directly through AS7
  Using similar arguments, D and E, would likely prefer the paths through A or B, and therefore not advertise their own paths that have a longer AS_PATH length/
  Barring specific policies configuration, e.g., a higher LOCAL_PREF for routes learned through one of the exits, router C will select the path through A as it has the smallest AS_PATH length (2) and is closer (cost of 6 vs. 9) than the other alternative, which is the path through B. This would not be affected by increasing the cost of the links AC & BC.

## Slide 30: Exercises
What path would router B use to reach AS8? What path would it use to reach AS9?
AS1 1.1.*
AS6 6.6.*
AS7 7.7.*
AS5 5.5.*
AS4 4.4.*
AS3 3.3.*
AS2 2.2.*
A
E
C
B
D
AS8 8.8.*
AS9 9.9.*
6
11
8
7
9
10
5
3.3.1.1
7.7.2.1
2.2.1.1
7.7.1.1
5.5.1.1
.1.*
.2.*
.3.*
.4.*
.5.*

## Slide 31: Exercises
What path would router B use to reach AS8? What path would it use to reach AS9?
  Router B would use the path AS8-AS2 advertised by router A since it is the path with the shortest AS_PATH length.
  It would use the path AS9-AS7 through router E since it is the path with the shortest AS_PATH length and router E is closer than router D that also advertises the same path.
AS1 1.1.*
AS6 6.6.*
AS7 7.7.*
AS5 5.5.*
AS4 4.4.*
AS3 3.3.*
AS2 2.2.*
A
E
C
B
D
AS8 8.8.*
AS9 9.9.*
6
11
8
7
9
10
5
3.3.1.1
7.7.2.1
2.2.1.1
7.7.1.1
5.5.1.1
.1.*
.2.*
.3.*
.4.*
.5.*

## Slide 32: Exercises
Show the forwarding table that would be created at router C, by OSPF and BGP working together. Show all prefixes and the interface used for forwarding packets to each each prefix (you may omit next-hop addresses). Assume the inter-router interfaces at C are numbered 1, 2, 3, 4 starting with the link to A, followed by the links to B and E, and finally the link to the subnet 1.1.3.*.
AS1 1.1.*
AS6 6.6.*
AS7 7.7.*
AS5 5.5.*
AS4 4.4.*
AS3 3.3.*
AS2 2.2.*
A
E
C
B
D
AS8 8.8.*
AS9 9.9.*
6
11
8
7
9
10
5
3.3.1.1
7.7.2.1
2.2.1.1
7.7.1.1
5.5.1.1
.1.*
.2.*
.3.*
.4.*
.5.*

## Slide 33: Exercises
Show the forwarding table that would be created at router C, by OSPF and BGP working together. Show all prefixes and the interface used for forwarding packets to each each prefix (you may omit next-hop addresses). Assume the inter-router interfaces at C are numbered 1, 2, 3, 4 starting with the link to A, followed by the links to B and E, and finally the link to the subnet 1.1.3.*.
  The forwarding table at router C is as shown on the right
1.1.1.* | 1
1.1.2.* | 2
1.1.3.* | 4
1.1.4.* | 1, 3
1.1.5.* | 3
2.2.* | 1
3.3.* | 2
4.4.* | 1
5.5.* | 3
6.6.* | 3
7.7.* | 3
8.8.* | 1
9.9.* | 3
AS1 1.1.*
AS6 6.6.*
AS7 7.7.*
AS5 5.5.*
AS4 4.4.*
AS3 3.3.*
AS2 2.2.*
A
E
C
B
D
AS8 8.8.*
AS9 9.9.*
6
11
8
7
9
10
5
3.3.1.1
7.7.2.1
2.2.1.1
7.7.1.1
5.5.1.1
.1.*
.2.*
.3.*
.4.*
.5.*

## Slide 34: Exercises
How could AS1 avoid carrying packets between AS2 and AS7? Might this have some “unintended” consequences?
AS1 1.1.*
AS6 6.6.*
AS7 7.7.*
AS5 5.5.*
AS4 4.4.*
AS3 3.3.*
AS2 2.2.*
A
E
C
B
D
AS8 8.8.*
AS9 9.9.*
6
11
8
7
9
10
5
3.3.1.1
7.7.2.1
2.2.1.1
7.7.1.1
5.5.1.1
.1.*
.2.*
.3.*
.4.*
.5.*

## Slide 35: Exercises
How could AS1 avoid carrying packets between AS2 and AS7? Might this have some “unintended” consequences?
  In order to avoid carrying packets from AS2 and destined to AS7, AS1 would simply not advertise to AS2 that it can reach prefix 7.7.*.
  The main consequence of this decision is that packets from AS2 (and AS4) will be required to take a longer detour (through AS8 and AS9) in order to reach AS7.
AS1 1.1.*
AS6 6.6.*
AS7 7.7.*
AS5 5.5.*
AS4 4.4.*
AS3 3.3.*
AS2 2.2.*
A
E
C
B
D
AS8 8.8.*
AS9 9.9.*
6
11
8
7
9
10
5
3.3.1.1
7.7.2.1
2.2.1.1
7.7.1.1
5.5.1.1
.1.*
.2.*
.3.*
.4.*
.5.*

## Slide 36: Exercises
Give an example illustrating how the routes computed by BGP can lead to packets traveling distances that are much longer than the shortest path distance between the sender and the receiver. How common do you think such sub-optimal paths are? What are some of the negative consequences of packets taking sub-optimal paths?
AS1 1.1.*
AS6 6.6.*
AS7 7.7.*
AS5 5.5.*
AS4 4.4.*
AS3 3.3.*
AS2 2.2.*
A
E
C
B
D
AS8 8.8.*
AS9 9.9.*
6
11
8
7
9
10
5
3.3.1.1
7.7.2.1
2.2.1.1
7.7.1.1
5.5.1.1
.1.*
.2.*
.3.*
.4.*
.5.*

## Slide 37: Exercises
Give an example illustrating how the routes computed by BGP can lead to packets traveling distances that are much longer than the shortest path distance between the sender and the receiver. How common do you think such sub-optimal paths are? What are some of the negative consequences of packets taking sub-optimal paths?
  Peering agreements can give rise to long detour, and so can instances of dual-homed customers. In both cases, possible shortcuts wont be advertised to peers or providers.
  Such sub-optimal paths used to be relatively common, but because the Internet’s topology has been “flattening”, their impact is now less than it used to be.
  Some of the negative consequences of sub-optimal paths are longer than necessary RTTs, which result in poorer TCP performance.
AS1 1.1.*
AS6 6.6.*
AS7 7.7.*
AS5 5.5.*
AS4 4.4.*
AS3 3.3.*
AS2 2.2.*
A
E
C
B
D
AS8 8.8.*
AS9 9.9.*
6
11
8
7
9
10
5
3.3.1.1
7.7.2.1
2.2.1.1
7.7.1.1
5.5.1.1
.1.*
.2.*
.3.*
.4.*
.5.*

## Slide 38: Exercises
One justification for BGP’s AS-hop-based metric is that it allows ISPs to conceal the topologies of their networks. Why do you think ISPs consider it important to keep this information secret? Do you think that these reasons are sufficient justification for the negative impacts of sub-optimal routing?

## Slide 39: Exercises
One justification for BGP’s AS-hop-based metric is that it allows ISPs to conceal the topologies of their networks. Why do you think ISPs consider it important to keep this information secret? Do you think that these reasons are sufficient justification for the negative impacts of sub-optimal routing?
  Exposing one’s internal topology makes denial of service attacks much easier to launch. In addition, no protocol would be able to scale well given the increasing size of the Internet, if it had to distribute the entire Internet topology.
  It is better to have a sub-optimal connectivity than no connectivity, which would likely be the case if we had selected a protocol that required exposing internal AS topologies.