## Slide 1: 6. The Open Network Lab
Overview and getting started
Building a network topology
Configuring routes and filters
Monitoring traffic
John DeHart, Jyoti Parwatikar and Jon Turner

## Slide 2: The Open Network Lab
Internet-accessible networking lab (onl.wustl.edu)
  built around set of extensible gigabit routers
  intuitive Remote Lab Interface (RLI): easy to get started
  extensive facilities for performance monitoring
Variety of resources
  16 five port Network Processor based Routers (NPR)
    highly configurable
    each has five processor cores reserved for plugins
  20 SoftWare Routers
    12 five port (1Gb/s per port) SWR
    8 two port (10Gb/s per port ) SWRs
      Configurable as 8 port (2.5 Gb/s ports) or 16 port (1 Gb/s ports)
  over 100 rack-mount servers that act as end systems
    including multicore servers with 8 cores and 48 cores
  VMs hosted on 20 12-core rack-mount servers

## Slide 3: Sample ONL Session
Network Configuration
Routing Table
Queue Lengths
Bandwidth Usage
Queue Parameters
Packet Losses
Router Plugin Commands
ssh window to host showing ping delays

## Slide 4: Overview of ONL
Remote access through the Internet using a graphical user interface called the RLI.
Provides access to variety of hardware resources
Experimental networks built with configuration switches

## Slide 5: Getting Started
Request an account at onl.wustl.edu
  read Getting Started page and look at tutorial pages
Download the RLI (version 8.4 is the latest as of 9/2015)
  to run RLI you must have Java Runtime Environment installed (version 1.6 or higher)
  RLI was just updated today (still version 8.4) for fix a small bug that showed up with our Lab2 configuration.
    So, download a new version before doing Lab2.
Create experimental network and save to a file
  details in a couple of slides

## Slide 6: Getting Started (continued)
Open an SSH connection to ONL with a tunnel for RLI
  on command line:
    ssh –L 7070:onlsrv:7070 <username>@onl.wustl.edu
Make a reservation using RLI and wait for confirmation
  note the start time in the confirmation message
After start time, select FileCommit in RLI
  open ssh connections to your ONL hosts and run applications
Unused reservations time out after 30 minutes

## Slide 7: Building a Basic Configuration
Select
  TopologyAdd PC1core AddHost1core
  and specify 3 hosts
Select
  TopologyAdd GigE Switch
  and specify single 1 Gb switch
Arrange hosts and switch
Select
  Press “Links Off” button
    Toggles it to “Links On”
  and wire hosts to switch
    When done, toggle to “Links Off”
Select
  FileSave As ...
  FileMake Reservation
  FileCommit (do not forget!!)

## Slide 8: Running Applications
Open ssh connections to hosts
  first ssh to onl.wustl.edu
  then run:
    > source ~/.topology
    > ssh $h1x1
Run standard apps
  on h1x1, type “ping h1x3”
  on h1x2, type “iperf –s”, then on h1x1, type “iperf –c h1x2”
Run basic client/server programs
  on h1x2, run java UdpEchoServer
  on h1x1, run java UdpEchoClient h1x2 9876 “hello world”

## Slide 9: Working with Larger Configurations
To include pair of NPRs (routers), select Topology Add IXPCluster Add NPRCluster
Note subnet numbering
Note multiple paths between routers

## Slide 10: Working With Routing Tables
Generate default routes to configure routing tables
Click on port to access specific table
Next hop specifies output port and next hop’s IP address
Change routes using OperationsEdit

## Slide 11: Configuring Packet Filters
address prefixes and ports
protocol and flags (TCP, UDP, … *=wildcard)
packet treatment
turn on/off
Select Filter Table

## Slide 12: Configuring Packet Filters
address fields
protocol and ports
output link
queue number

## Slide 13: Monitoring Traffic
select desired monitor variable
To add new real-time chart
to select outgoing packet rate at a port
observing ping traffic from h4x2 to h6x1
STILL OLD
VERSION OF RLI
But very close to current

## Slide 14: Hosts with Multiple Interfaces
ONL hosts have two interfaces
  data interface used for experimental network
    names of form hAxB. and addresses of form 192.168.A.B addresses,
  control net interface used to talk to ONL servers
    names of form pc1coreNN, addresses of form 10.0.x.y
    File ~/.topology defines shell variables of form $hAxB that map to control net names
To force server connections to use a specific interface, bind socket to desired interface’s IP address
  forces communication to server to come through specified iface
If socket left “unbound”, system uses wildcard interface
192.168.1.3
10.0.x.y
control net

## Slide 15: Using the ONL Web Site
Testbed Status
My Reservations
Resource Availability
Etc.
Show examples…

## Slide 16: Using the Linux Command Line
ONL hosts all run Linux
  to use them effectively, need to be familiar with the command-line interface provided by the “shell” (specifically, bash)
Common commands
  ls to list files in a directory (aka folder)
  cd to change the current working directory
  more to examine contents of a file
  ssh to open an ssh connection to another computer
  man to get documentation for a given command
    type “man ls” to learn how to use the ls command
  See http://www.ee.surrey.ac.uk/Teaching/Unix/index.html and http://www.gnu.org/software/bash/manual/bash.html
You need to invest some time up-front to learn Linux
  but, you’ll be much more productive once you do

## Slide 17: Using Wireshark in ONL
Wireshark is implemented using the X-windows system
  ssh supports tunneling of X-windows commands, allowing you to run Wireshark in ONL with GUI running on laptop
On Urbauer lab computers
  first type “startxwin” in a command prompt window
  this starts new window; in this window, type
    ssh –X userName@onl.wustl.edu source /users/onl/.topology ssh –X onlHostname (e.g. $h4x2) sudo wireshark
  this starts Wireshark on remote machine, but your local computer acts as the display for remote instance of Wireshark
Can use this with other X-windows applications also

## Slide 18: LAB2: What you will be given
For your assignments you’ll be given a topology file in your bitbucket repository:
  lab2/cse473-lab2.onl

## Slide 19: LAB2: What you will be given (continued)
You will also be given an assignment document:
  lab2/lab2.pdf
And a lab report document:
  lab2/lab2report.docx
  Which has VERY specific directions. Follow them.

## Slide 20: LAB2: What you will be given (continued)
More from lab report document:
What is a plugin?
  The Network Processors used in the routers have 5 microengines allocated to hosting user specific code called plugins.
For Lab2 we are using a delay plugin we have written for simulating things like link delay. It is preconfigured in your topology.
And more from the lab report document:
Back to what we said earlier about packet filters…

## Slide 21: Configuring Packet Filters
address prefixes and ports
protocol and flags (TCP, UDP, … *=wildcard)
packet treatment
turn on/off
Select Filter Table

## Slide 22: LAB2: What you will be given (continued)
Show example …
  Load Lab2
  Reserve
  Commit
  Monitoring windows
  Hover over labels and show different traces come to the foreground.
  Etc.