## Slide 1: BCI2000: 2D Control

## Slide 2: Getting Started
Follow the Passive Stimulus Presentation Data Collection Tutorial on the wiki
  However, when the tutorial tells you to run StimPresentation run IpsiHand_Cursor Task instead
  Also when you load the parameters, load IpsiHand_LPR_CursorTask_CR instead

## Slide 3: Getting Data
Before pressing start, make sure that ‘cursor task’ (the gridded window in the upper-left corner) is visible
To move the ball to the right move your right hand.
  Be sure to not move your head, blink, swallow, or move other muscles
  Move your hand in a way that takes effort (eg. Play an imaginary piano, touch individual fingers together…)
To move the ball to the left do not move at all
In between trials it’s ok to blink

## Slide 4: Analyzing the Data
Follow the directions in User Tutorial: Performing Offline EEG Analysis
  After instructed to click the “add” button, navigate to data\[your initials]\[most recent data file] instead of the three files suggested by the tutorial
  For Condition 1 enter states.TargetCode ==1
  For Condition 2 enter states.TargetCode ==2
  For Trial Change Condition enter Feedback ==1
  Set Label 1 to “Pause” and Label 2 to “Right hand”
Looking at the correlation maps, you want to see a few brightly colored bands in the sections between 9 and 24 Hz, and channels 1-4
The greater the correlation the better! Keep practicing and try to get your correlations above 0.20
Repeat data collection and analysis steps multiple times until you feel like you have some 1D control over the ball.

## Slide 5: Homework 1: Troubleshooting in BCI2000
Run the CursorTask batch file
Load the parameters called CursorTask_WithErrors
Fix the errors and press set Config
If you still get errors, try again!

## Slide 6: Homework 2: Adjusting the Linear Classifier
Run the cursor task batch file and load the parameters IpsiHand_LPR_CursorTask_CR
Change the Linear Classifier so that you have 2D control (add electrodes mapping to output channel 2)
  Output channel 2 can be different frequencies or different electrodes than output channel 1.
  Change it up until you have at least a little bit of control over the ball
  If you have complete control over the ball, you achieved the goal of the project!

## Slide 7: Homework 3: Improving 2D Control
Open a data set in matlab using the command like:
[signal states parameters] = load_bcidat('C:\Users\Colleen\Dropbox\IpsiHand\BCI2000\data\CR001\CRS001R04.dat');
  Except adjust the path so that MatLab loads your data file
The variable “signal” should have 14 columns for the 14 electrodes
  Create a new matrix made up of the electrodes from the signal that you care about

## Slide 8: Improving 2D Control continued
Run the command: [coeff,score] = princomp(signal_new);
Look at the coeff matrix
  The first column is the best weights for each electrode in the 1st dimension and the second column is the best weights in the 2nd dimension
Go back to the linear classifier and try the new weights and see if CursorTask becomes easier
  Repeat the directions from the slide “Analyzing the Data”

## Slide 9: Solution Homework 1
Make the spatial filter a 4x4 identity matrix
Repeat the first number for NormalizerOffsets, NormalizerGains, and Adaptation
Add a high pass filter
Change the SourceChOffset to fourteen zeros
Change the SourceChGain to fourteen ones

## Slide 10: Possible Solution Homework 2
 | Input Channel | Input element (bin) | Ouput Channel | Weight
1 | 1 | 12Hz | 1 | -0.025
2 | 2 | 1Hz | 1 | -0.025
3 | 3 | 12Hz | 1 | -0.025
4 | 4 | 12Hz | 1 | -0.025
5 | 11 | 12Hz | 2 | -0.025
6 | 12 | 12Hz | 2 | -0.025
7 | 13 | 12Hz | 2 | -0.025
8 | 14 | 12Hz | 2 | -0.025